## Slide 1: PNU WiFi 무선랜 서비스 품질 분석 및 개선 연구
부산대학교 정보컴퓨터공학부
201524412 곽민수
201624419 김도형
201724537 이예경

## Slide 2: 목차
기존 연구 분석
연구 목적
과제 진행 상황
  데이터 수집 및 정리
  시뮬레이션
    시각화
    설정
    실행
  UML
    시각화
    설정 및 실행
  시뮬레이션 수정 후 결과
  차후 계획
구성원 역할 분담 및 진척도
부록

## Slide 3: 기존 연구 분석
WiFi 사용 불편 원인 분석
  기존 연구에서 PNU-WiFi 사용 불편의 다양한 원인 중 AP 집중 현상에 초점
  불균형 위치를 찾기 위해 캠퍼스 전체 건물을 용도에 따라 네 그룹으로 분류
  이용자(Client) 데이터를 분석하여 각 그룹에서 불균형이 가장 심한 층 선정
문제점
  AP가 설치된 위치적 특성, 사용 목적 등을 고려했을 때 불필요한 AP 존재
  지나치게 많은 AP로 인해 자원의 불균형 발생
그림1. 새벽벌 도서관 1층의 세션 분포 그래프
그림2. 중앙 도서관 1층 도면

## Slide 4: 연구목적
연구 목적
  STA의 Throughput을 향상시키는 것
  필요한 AP의 최소 개수 산정, 최적의 배치 방법 제시
  AP 서비스 음영 지역 최소화
제약사항
  모든 STA를 어떠한 AP와 연결할 것
  모든 STA이 일정 수준의 Throughput을 넘을 것
  AP 커버리지가 건물 면적의 00%보다 클 것
그림3. AP 배치 예시

## Slide 5: 과제 진행 상황
시뮬레이션 코드 분석
  각 변수의 역할과 함수의 기능 분석
  Configuration, Visualization, Execution
  시뮬레이션 실행 시간 문제가 있음
수집 데이터 분석
  새벽벌 도서관에 대해 우선적으로 진행
  AP 사용 현황 데이터를 수집, 통계
  건물 시각화, 통계 낸 데이터를 적용하여 실제 환경 모사
그림4. 새벽벌 도서관 시각화
그림5. 데이터 통계 예시
Notes: Path Loss: 현재 건물, 벽 등을 고려한 상태.

## Slide 6: 데이터 수집 및 정리
원본 데이터
  기간: 2019년 6월 1일 ~ 2019년 12월 31일
  시간: 0~23시까지 1시간 간격
  범위: 2.4GHz / 5GHz
  공통 데이터: AP Name, Map Location(건물명), Time 등
시뮬레이션에 필요한 데이터
  Peak Number of Users:
    단위 시간동안 AP에 연결된 최대 이용자 수
  Channels in Use:
    단위 시간동안 사용된 채널
그림6. AP 원본데이터

## Slide 7: 데이터 수집 및 정리
데이터 정리
  이용자 수는 요일, 시간에 따라 주기성을 가짐
  평일, 주말로 구분하여 1시간마다 평균
    Map Location을 이용하여 건물별 데이터 추출
    AP 이름을 리스트에 저장, AP별로 데이터 정리
    Weekday를 이용 평일 주말로 구분
    Peak Number of Users 추출
    2.4GHz와 5GHz 이용자 수 합
    24개 단위로 데이터 분할
    시간대별로 이용자 수 평균
그림7. 새벽벌 도서관의 이용자 수 통계 예시
AP 이름
평일 주말
시간

## Slide 8: 시뮬레이션
MATLAB WLAN Toolbox
  주요 기능:
    네트워크 및 채널을 구성하여 시나리오 모델링
    다중 노드 WLAN 시스템을 시뮬레이션하고 통계 시각화
  시나리오:
    노드간의 거리와 벽과 바닥 수를 기반으로 PathLoss 모델링
    Channel Manager
    Application Layer
    MAC Layer
    Physical Layer
  결과 섹션:
    처리량
    대기 시간
    패킷 손실
그림8. 시뮬레이션 예시

## Slide 9: 시뮬레이션
시각화
건물(벽, 바닥) 생성
노드 생성
설정
노드 설정
실행
Network Simulator
Stats Logger
시각화
Channel Manager
Path Loss
Application Layer
MAC Layer
Node
Traffic
AP
Station
Packet 전송
안테나 설정

## Slide 10: 시뮬레이션 (시각화)
각 Point 들을 연결한 삼각형으로 면 제작
(0,0,0)
(10,0,0)
(10,10,0)
(0,10,0)
(0,0,10)
(10,0,10)
(0,10,10)
(10,10,10)

## Slide 11: 시뮬레이션 (시각화)
Node Position 설정
AP(5,5,5)
STA(3,3,3)

## Slide 12: 시뮬레이션 (설정)
송신 안테나 설정
  위치 : (5,5,5)
  파워 : 10dBm
  등방향성 : True
  주파수
    2.4GHz : 2412 ~ 2472 (MHz)
    5Ghz : 5180 ~ 5825 (MHz)
    6Ghz : 5945 ~ 7105 (Mhz)

## Slide 13: 시뮬레이션 (설정)
수신 안테나 설정
  위치 : (3,3,3)
  수신감도 : -100dBm
  등방향성 : True

## Slide 14: 시뮬레이션 (설정)
Node와 Traffic에 대한 설정 부여
  Node : MAC, PHY Configuration*
  Traffic : Application Configuration*
* 부록 참고

## Slide 15: 시뮬레이션 (설정)
Path Loss 계산 및 범위 설정
  최대 90m
  격벽에 대해 고려

## Slide 16: 시뮬레이션 (설정)
각 계층 생성
Application Layer
MAC Layer
PHY Layer

## Slide 17: 시뮬레이션 (실행)
Application Layer에서 Packet 생성 후 MAC Layer의 Queue로 전송
  Next Invoke Times(Microsecond)를 통해 다음 Packet 생성 시간 설정
Application Layer
MAC Layer
PHY Layer
Application Layer
MAC Layer
PHY Layer
Transmitter
Receiver
ON
OFF
Next Inovke Times
Packet 생성
MAC Queue
1
2
3
4

## Slide 18: 시뮬레이션 (실행)
MAC Layer (Channel Manager)
  AP와 STA 개수에 대해 차트 생성 (현재 Single User)
Application Layer
MAC Layer
PHY Layer
Application Layer
PHY Layer
Transmitter
Receiver
MAC Layer
(Channel Manager)
Backoff
Time Line
AIFS
T x R
AIFS (Arbitration Inter Frame Space)
: 데이터의 속성에 따른 대기시간
Back Off
: Slot Time 만큼의 추가 대기시간
AIFS
Backoff
Channel Matrix H

## Slide 19: 시뮬레이션 (실행)
Frame
전송을 위한 PHY Layer 추상화
  Waveform 전환 및 전송 시간 제공
Application Layer
MAC Layer
PHY Layer
Application Layer
PHY Layer
Transmitter
Receiver
MAC Layer
TxBuffer
RxBuffer
Waveform
Backoff
Time Line
AIFS
Data
RxAbstract
TxAbstract
Time

## Slide 20: 시뮬레이션 (실행)
Buffer에 따라 수신 여부 판단
Application Layer
MAC Layer
PHY Layer
Application Layer
PHY Layer
Transmitter
Receiver
MAC Layer
MAC Layer
TxBuffer
RxBuffer
Frame
Backoff
Data
Time Line
AIFS
RxAbstract
TxAbstract

## Slide 21: 시뮬레이션 (실행)
각 Node 마다 Simulation 진행
STA1
STA2
STA3
Backoff
Data
Time Line
AIFS
SIFS
ACK
AIFS
Backoff
Data

## Slide 22: UML (시각화)
ScenarioParameters
BuildingLayout RoomSize NumRxPerRoom
hTGaxResidentialTriangulation
ScenarioParameters
tri
hDropNodes
ScenarioParameters
apPositions staPositions
hLoadConfiguration
ScenarioParameters apPositions staPositions
nodeConfigs trafficConfigs
hCreateSitesFromNodes
nodeConfigs
txs rxs
hVisualizeScenario
tri trx rxs apPositions
시뮬레이션 시각화
hTGaxResidentialPathLoss
‘Triangulation’ = tri ‘ShadowSigma’ = 0 ‘FacesPerWall’ = 1
propModel
hCreatePathlossTable
txs rxs propModel
pl tgaxIndoorPLFn
■ : AP
■ : Station
hCreateWLANNodes
nodeConfigs trafiicConfigs simulationTime tgaxIndoorPLFn
wlanNodes

## Slide 23: UML (설정 및 실행)
hLoadConfiguration
ScenarioParameters apPositions staPositions
nodeConfigs trafficConfigs
hCreateWLANNodes
nodeConfigs trafiicConfigs simulationTime tgaxIndoorPLFn
wlanNodes
hApplication
NodeID FillPayload
Application Layer
hTGaxChannelManager
Channel ChannelManager
OFDM
hWLANNode
NodeID NodePosition RecieverRange Frequencies PHYTx PHYRx Channel Application
Application MAC Layers Physical Layers
wlanNodeConfig.mat
MAC PHY
wlanTrafficConfig.mat
hWirelessNetworkSimulator
netwotkSimulator wlanNodes simulationTime statsLogger
Chart
run
statistics.mat
hStatsLogger
NumNodes NodeNames Nodes
Frequencies Initialize StatsLog
hEDCAMAC
wlanNodeConfig
MAC

## Slide 24: 시뮬레이션 수정 후 결과
평면도를 바탕으로 실제 크기와 유사하게 모델링
실제 도서관의 AP 위치를 고정
AP 범위 내에서 STA를 랜덤 위치에 생성
AP 커버리지 표시할 예정
그림9. 주말 오전 6시 새벽벌 도서관 시각화

## Slide 25: 시뮬레이션 수정 후 결과
결과에 필요한 데이터
  전송한 패킷 수, 수신된 패킷의 DataBytes,
  전송 성공한 패킷 수 (Success),
  전송 실패한 패킷 수 (Fail),
  전송 재시도한 패킷 수 (Retry)
총 전송한 패킷 수 = Success + Fail + Retry
  Throughput
  = (DataBytes * 8) / Simulation Time
  Packet Loss Ratio = (전송 패킷 수 – Success) / 전송 패킷 수
  Packet Delivery Ratio = Success / 전송 패킷 수
  Packet Error Ratio = Fail / 전송 패킷 수
  Packet Latency
  = 해당 패킷이 전송완료되기까지의 시간 – 패킷 전송을 시작했을 때 시간
그림10. 시뮬레이션 결과 차트

## Slide 26: 차후 계획
Node Configuration에 대한 추가적인 이해 필요
  WiFi 종류에 대한 설정
  Single User & Multi User
시뮬레이션 시간 성능 개선
  Frame이 전송되는 동안 계속해서 새로운 Frame을 만들어 Queue 대기하고 있음
알고리즘 구현
  연구실에서 특허로 진행 중인 최적 AP 배치 알고리즘 적용 예정
그림11. Node 진행 상황
그림12. Queue에 대기중인 Frame 수

## Slide 27: 구성원 역할 분담 및 진척도
곽민수
  MATLAB을 이용한 부산대학교 교내 건물 환경 구현 완료
    새벽벌 도서관의 바닥 및 벽 등 물리적 요소 구현
    실제 건물 크기에 맞게 구현
  MATLAB을 이용한 부산대학교 교내 AP 환경 구현 완료
    AP 가용 범위 계산 및 적용
    각 AP 범위 내 Station 랜덤 위치 생성
  최적화 정보 시각화 시스템 개발 예정
    웹 사이트 제작
이예경
  2019년도 PNU WiFi 사용 현황 데이터 수집 및 정리 완료
    시간대별 이용자 수 도출
    요일별 이용자 수 도출
  수집 데이터를 시뮬레이션에 적용 완료
  시뮬레이션 평가 결과 데이터화 예정
김도형
  시뮬레이션 동작 및 결과 시각화 완료
    Path Loss
    Packet Delivery Ratio
    Packet Error
    Channel Distribution
    Throughput
  시뮬레이션 Channel Utilization 시각화 중
  시뮬레이션 동작 시간 개선 중
    불필요한 시각화 제거
    전송 내역 정리

## Slide 28: 부록
wlanNodeConfig (MAC Layer)
  NodePosition
    Description: Position of the node
    Value: Vector of [x,y,z] format, in units of meters
    Default: [0 0 0]
  TxFormat
    Description: Transmitting packet format
    Value: Accepts "NonHT", "HTMixed", "VHT", "HE_SU", "HE_EXT_SU". You can also set the value to the enum type from hFrameFormatsEnum.
    Default: "HE_SU"
  Bandwidth
    Description: Channel bandwidth
    Value: Accepts 20, 40, 80, or 160.
    Default: 20
  TxMCS
    Description: Specifies the modulation and coding scheme (MCS) index that is used for transmitting the frame. This value applies only when RateControl is set to "FixedRate".
    Value: When TxFormat is set to "HE_SU", accepts numbers in the range [0,11]. When TxFormat is set to "VHT" and NumTxChains is not 3 or 6, accepted range is [0,9]. When TxFormat is set to "VHT" and NumTxChains is 3 or 6, accepted range is [0,8]. When TxFormat is set to "HTMixed" or "NonHT", accepted range is [0,7]. When TxFormat is set to "HE_EXT_SU", accepted range is [0,2]. For "HTMixed", the MCS value input in the range [0,7] is automatically mapped to the index in the range [0,31] based on the NumTxChains value.
    Default: 7
  NumTxChains
    Description: Number of transmit chains.
    Value: When TxFormat is set to "VHT" or "HE_SU", accepts numbers in the range [1,8]. When TxFormat is set to "HTMixed", accepted range is [1,4]. When TxFormat is set to "HE_EXT_SU", accepted range is [1,2]. When TxFormat is set to "NonHT", only 1 transmit chain is allowed.
    Default: 1

## Slide 29: 부록
  MPDUAggregation
    Description: Flag that enables MPDU aggregation when set to true. Applies only when TxFormat is set to "HTMixed" format.
    Value: A logical scalar (true or false)
    Default: true
  DisableAck
    Description: Flag indicating the transmitter does not solicit acknowledgment for the frame.
    Value: A logical scalar (true or false)
    Default: false
  MaxSubframes
    Description: Specifies the maximum number of subframes that can be aggregated in the A-MPDU.
    Value: Accepts a number in the range [1,256].
    Default: 64
  RTSThreshold
    Description: Specifies the threshold length of the frame after which RTS/CTS protection is used for data transmission. Applies only when DisableRTS is set to false.
    Value: Accepts a number in the range [0,65536].
    Default: 65536
  DisableRTS
    Description: Flag that disables RTS/CTS exchange for all the data transmissions when set to true.
    Value: A logical scalar (true or false)
    Default: false
  MaxShortRetries
    Description: Specifies the retry limit for frames less than RTS threshold.
    Value: Accepts a number in the range [0,32].
    Default: 7

## Slide 30: 부록
  MaxLongRetries
    Description: Specifies the retry limit for frames greater than RTS threshold.
    Value: Accepts a number in the range [0,32].
    Default: 7
  BasicRates
    Description: Set of data rates representing basic rate set
    Value: Accepts a vector of data rate values. The values must be from the set [6, 9, 12, 18, 24, 36, 48, 54].
    Default: [6 12 24]
  Use6MbpsForControlFrames
    Description: Flag that forces to use 6 Mbps data rate for all control frames ignoring the values in BasicRateSet.
    Value: A logical scalar (true or false)
    Default: false
  BandAndChannel
    Description: Operating band and channel number
    Value: A cell array of vector in the format {[x, y]} where x = band, y = channel number. The value of x can be 2.4, 5, or 6. The value of y can be any valid channel number.
    Default: [2.4, 6]
  CWMin
    Description: Minimum value for the contention window range for each access category.
    Value: A row vector of size 4, indicating the CWMin values for four access categories. Each value in the row vector must be in the range [1,1023].
    Default: [15 15 7 3]
  CWMax
    Description: Maximum value for the contention window range for each access category.
    Value: A row vector of size 4, indicating the CWMax values for four access categories. Each value in the row vector must be in the range [1,1023].
    Default: [1023 1023 15 7]

## Slide 31: 부록
  AIFSSlots
    Description: Number of arbitrary interframe space (AIFS) slots for each access category.
    Value: A row vector of size 4, indicating the number of AIFS slots for four access categories. Each value in the row vector must be in the range [2,15].
    Default: [3 7 2 2]
  RateControl
    Description: Rate control algorithm to use
    Value: Accepts either "FixedRate" or "ARF"
    Default: "FixedRate"
  PowerControl
    Description: Power control algorithm to use
    Value: Accepts only "FixedPower"
    Default: "FixedPower“
wlanNodeConfig(PHY Layer)
  TxPower
    Description: Transmit power
    Value: A scalar number representing the transmit power in dBm
    Default: 15
  TxGain
    Description: Transmit gain
    Value: A scalar number representing the transmit gain in dB
    Default: 1

## Slide 32: 부록
  RxGain
    Description: Receive gain
    Value: A scalar number representing the receive gain in dB
    Default: 0
  EDThreshold
    Description: Energy detection threshold value
    Value: A scalar number representing the threshold in dBm
    Default: -82
  RxNoiseFigure
    Description: Receiver noise figure
    Value: A scalar number representing the noise figure in dB
    Default: 7
  ReceiverRange
    Description: Packet reception range
    Value: A scalar number representing the range in meters
    Default: 1000
  FreeSpacePathloss
    Description: Flag that enables free space pathloss when set to true
    Value: A logical scalar (true or false)
    Default: true
  PHYAbstractionType
    Description: Type of PHY abstraction
    Value: Accepts either "TGax Simulation Scenarios MAC Calibration" or "TGax Evaluation Methodology Appendix 1"
    Default: “TGax Evaluation Methodology Appendix 1”

## Slide 33: 부록
wlanTrafficConfig (Application)
  SourceNode
    Description: ID of the source node transmitting the packet, at which the application is running. To configure multiple transmitters in the network, this structure must be replicated and the structures should have different SourceNode values
    Value: A scalar number less than or equal to number of
    nodes in the network
    Default: 1
  DestinationNode
    Description: ID of the destination node to which the packet is intended. To transmit packets destined to two different nodes from the same source node, replicate the structure two times, and the two structures in the array must contain the same value for SourceNode and different values for DestinationNode.
    Value: A scalar number less than or equal to number of nodes in the network
    Default: 4
  PacketSize
    Description: Size of the generated application packets
    Value: A scalar number in the range [1,2034]
    Default: 1500
  DataRateKbps
    Description: Rate at which application packets are generated
    Value: A scalar number representing the data rate in Kbps
    Default: 600000
  AccessCategory
    Description: Access category where 0 represents best-effort traffic (BE), 1 represents background traffic (BK), 2 represents video traffic (VI), 3 represents voice traffic (VO).
    Value: A scalar number in the range [0,3]
    Default: 0